08/10/2012		CAA(B)/MBD2

ED. 51	MANDATORY MODIFICATIONS / INSPECTIONS RECORD	SEQUENCE NUMBER/

| AD / CN / TN / NT | REF. | SUBJECT / SPECIFICATIONS | COMPLIANCE |
| --- | --- | --- | --- |
| ALTERNATE |  |  | 1X | METHOD | DATE & TIME | BY |
| FAA AD 78-18-04 | SB Bendix 584, 587, 590A, 600 | BENDIX: Magneto loss of ignition D-2000, D-2200. |  |  |  |  |
| FAA AD 79-12-07 | SB Bendix 606 | BENDIX: Magneto green distributor block bushings D-2000, D-2200, 6 and 8 cyl. |  |  |  |  |
| FAA AD 79-18-06 | SB Bendix 584B, 605A | BENDIX: Magneto Loss of ignition model D-2000, D-2200. |  |  |  |  |
| FAA AD 80-17-14 | SB Bendix 605A | BENDIX: Loss of ignition D-2000, D-2200. |  |  |  |  |
| FAA AD 82-11-05 | SB Bendix 617 | BENDIX: Magneto distributor gear electrodes D-2000, D-2200. |  |  |  |  |
| FAA AD 82-20-01 | SB Bendix 623 | BENDIX: Magneto Impulse coupling flyweights. |  |  |  |  |
| CAA(B)NT/TN 92-01R2 |  | MAGNETO: Entretien périodique. MAGNETO: Periodiek onderhoud. |  | 500h 120m |  |  |
| FAA AD 96-12-07 | MSB 639 MSB 645 | TCM / BENDIX: Magneto impulse coupling. |  | 500h |  |  |
| Sup. by AD 2005-12-06 |  |  |  |  |  |  |
| FAA AD 2005-12-06 | MSB 645 SB 649 SIL 648 | TCM / BENDIX: Magneto impulse coupling installed on Lycoming AEIO-540, HIO-540, IO-540, O-540 and TIO-540 engines |  | Riveted: 100h Snap ring: 500h |  |  |
| APPLIANCES | MAGNETO | DUAL 2000 | S.N°.: | O.H. Date / By | INSTALLATION SEE CARDEX | SHEET |
|  |  | Model: | P.N°.: |  |  | 1 |

ED. 51	CARDEX

| Fitted on A/C OO- |  | Component : |  |  |
| --- | --- | --- | --- | --- |
|  |  | Model : |  |  |
|  |  | P.N°. : |  | Removal each : |  | for : |  |
|  |  | S.N°. : |  | or each : |  | for : |  |
|  | INSTALLATION | REMOVAL | REMOVAL DUE |
|  | Date | A/C TT | Comp TT | Comp. T.S.O. | Reason removal | Date | A/C TT | Comp TT on A/C | Comp TT | Comp T.S.O. | A/C TT | Date |